## Slide 1: COMPUTER NETWORKS: Classful IP Addressing
Muhammad Sad Al Munir
Tracking ID: 480484

## Slide 2: Index
IP addressing
IPv4 addressing
Classful IP addressing
Types of classes in Classful IP addressing

## Slide 3: IP addressing
An address having information about how to reach a specific host, especially outside the LAN
IPv4 addresses
32 bits unique address
Dotted decimal / hexadecimal notations
128.228.0.1

## Slide 4: Terms
Net ID
Broadcast ID
Host ID
Mask

## Slide 5: Classful IP addressing
Class A, B, C, D &E
Class D used for multicasting
Class E reserved

## Slide 6: IPv4 address notations
32 bits 01111100 00000101 10101010 11110000
4 Octets 01111100 00000101 10101010 11110000
Dotted Notation 01111100.00000101.10101010.11110000
Dotted Decimal Notation 124.5.170.240

## Slide 7: Finding the class in binary notation
Class A
Class B
Class C
Class D
Class E
First Byte | Second Byte | Third Byte | Fourth Byte
0 |  |  | 
10 |  |  | 
110 |  |  | 
1110 |  |  | 
1111 |  |  | 

## Slide 8: Finding the class in decimal notation
Class A
Class B
Class C
Class D
Class E
First Byte | Second Byte | Third Byte | Fourth Byte
0 to 127 |  |  | 
128 to 191 |  |  | 
192 to 223 |  |  | 
224 to 239 |  |  | 
240 to 255 |  |  | 

## Slide 9: IPv4 address space
Class | Network Mask | Network Bits | Number of Networks | Host Bits | Maximum hosts per network
A | 255.0.0.0 | 8 | 28-1 | 24 | 224 - 2
B | 255.255.0.0 | 16 | 216-2 | 16 | 216 - 2
C | 255.255.255.0 | 24 | 224-3 | 8 | 28 - 2

## Slide 10: Calculation of Network ID
IP address 166.75.229.22/16
Network musk /16
Network musk 255.255.0.0
IP address bits 1010 0110.0100 1011.1110 0101.0001 0110
                AND
Masking bits 1111 1111.1111 1111.0000 0000.0000 0000
Network ID 1010 0110.0100 1011. 0000 0000.0000 0000
Network ID 166.75.0.0

## Slide 11: Example
Find the class and network ID from the following address spaces
158.228.1.108
193.13.14.128

## Slide 12: Solution
158.228.1.108
128<158<191 Class B, Network ID: 158.228.0.0
193.13.14.128
          191<193<223 Class C, Network ID: 193.13.14.0

## Slide 13: Notes
Millions of Class A addresses wasted
Many Class B addresses wasted
Number of addresses in a Class C block smaller than the needs of most of the organizations
Class D addresses used for multicasting
Class E addresses reserved for special purposes